## Slide 1
DESIGN OF A SITE SELECTION SYSTEM FOR A LITHIUM PROCESSING PLANT IN ZIMBABWE
HIT300 – DESIGN AND MAKE PROJECT
TIVAKUDZE MAGUNDA – H240646A
Supervisor: Eng Gwatidzo
Industrial and Manufacturing Engineering

## Slide 2: PROBLEM BACKGROUND
Lithium powers electric-vehicle and grid-storage batteries; global demand has grown sharply.
Zimbabwe banned unprocessed lithium exports in December 2022, committing the country to beneficiation.
Main sources are Bikita, Arcadia (Goromonzi) and Zulu (Insiza); a plant draws ore from several mines.
Infrastructure is uneven: rail, grid and water differ sharply between districts.
Hidden factors (water, power, tailings, community response) decide whether a plant succeeds.
Without a written method, factor weights shift with whoever is in the room.

## Slide 3: LITERATURE REVIEW
Multi-criteria decision making: weighted scoring and AHP are mature but need a skilled analyst (Belton and Stewart, 2002).
GIS suitability analysis: strong for finding where a plant could go, weak at gates, costs and scenarios.
Facility location and transportation models: give cost-minimal allocation (Daskin, 2013; Eiselt and Marianov, 2011).
Feasibility gates: hard constraints that no score can compensate for.
Research gap: no tool joins gates, scoring, optimisation and reporting for lithium in Zimbabwe.
Second gap: existing methods assume an analyst; decision makers need inputs and outputs only.

## Slide 4: PROBLEM STATEMENT
Zimbabwe has no structured, transparent and repeatable tool for selecting lithium processing plant sites.
Unstructured judgement hides trade-offs and inflates lifetime operating costs.
Utility, land and environmental risks show up only after construction begins.
The decision is once-off with a decades-long tail, so it must be right the first time.
“Right” means transparent, auditable and comprehensive, not merely confident.

## Slide 5: AIM
To design a site selection system for a lithium processing plant in Zimbabwe that combines a structured criteria framework, a mathematical optimisation model and a user-facing computational tool to produce transparent and defensible site recommendations.

## Slide 6: OBJECTIVES
1
Criteria framework
Define the industrial, logistical, utility, land and environmental factors, with the evidence required to assess each.
2
Optimisation model
Formulate a transparent model for facility selection and feedstock allocation with stated capacity, supply and feasibility constraints.
3
Computational system
Report feasibility-gate outcomes, estimated annual costs, allocation decisions and sensitivity to changing assumptions.

## Slide 7: RESEARCH METHODOLOGY
Design-science approach: the artefact is a decision support system; every design choice is explicit and justified.
Problem identification
Criteria definition
Gate specification
Scoring and optimisation model
Software design and demonstration
Evaluation: demonstration on a worked scenario; outputs checked for correctness, completeness and explainability.
Data: criteria from siting literature adapted to Zimbabwe; site and mine data entered by the user; OpenStreetMap basemap.
Missing evidence: never defaulted; a site with no water data fails the water gate.

## Slide 8: CONCEPT 1: DESKTOP GIS WEIGHTED OVERLAY
Prepare spatial layers
Weighted overlay in QGIS / ArcGIS
Analyst interprets suitability map
Manual write-up
Strength: excellent for regional screening and for discovering where a plant could go.
Weakness: no gate logic, no allocation optimisation and no repeatable interface; the analyst must rebuild the workflow for every new question.
REJECTED: fails gates, optimisation and interface requirements

## Slide 9: CONCEPT 2: PYTHON, FLASK AND POSTGIS
Forms enter sites, mines, weights
Feasibility gates (Python)
Scoring + LP allocation (SciPy / PuLP)
Report on Flask pages
Strength: meets every mandatory requirement; PostGIS offers true spatial queries.
Weakness: two languages and two frameworks, plus a database server to install, secure and back up, for spatial needs that are only simple distances.
RUNNER-UP: passed screening, weighted score 66.5 / 100

## Slide 10: CONCEPT 3: NEXT.JS, SQLITE AND OPENSTREETMAP
Next.js UI: sites, mines, weights
SQLite store via Prisma
Feasibility gates
Weighted score + allocation
Results, map, sensitivity
Strength: one language end to end, zero-administration database, free map tiles and an auditable pipeline.
Weakness: SQLite does not suit heavy concurrent use and the solver is home-built, which is acceptable at this problem size.
SELECTED: passed screening, weighted score 90.5 / 100

## Slide 11: CONCEPT 4: MATLAB OR EXCEL AHP TOOL
Pairwise comparison matrices
Derive weights, check consistency
Weighted scores per site
Excel / MATLAB tables and charts
Strength: rigorous weight derivation with a built-in consistency check.
Weakness: files are fragile to share, anyone can edit logic silently, gates cannot be enforced and there is no scenario database or map.
REJECTED: fails gates and interface (AHP kept as future work)

## Slide 12: CONCEPT 5: MACHINE LEARNING SCORING
Feature engineering per site
Train classifier on labelled sites
Predict suitability probability
Rank sites
Strength: scales to large, repetitive prediction tasks.
Weakness: no labelled dataset of good and bad sites, a black-box result cannot explain why a site won, and the problem is only a handful of candidates.
REJECTED: fails explainability and has no gate mechanism

## Slide 13: CONCEPT SELECTION
Mandatory requirement | C1 | C2 | C3 | C4 | C5
Criteria framework with evidence | ✓ | ✓ | ✓ | ✓ | –
Feasibility gates | – | ✓ | ✓ | – | –
Allocation optimisation | – | ✓ | ✓ | ✓ | –
Usable decision-maker interface | – | ✓ | ✓ | – | –
Explainable output | ✓ | ✓ | ✓ | ✓ | –
Result | Fail | Pass | Pass | Fail | Fail
Criterion (weight) | C2 | C3
Deployment, maintenance (25%) | 60 | 90
Single language (20%) | 55 | 95
Persistence simplicity (20%) | 70 | 90
Mapping cost (15%) | 75 | 90
Auditability (20%) | 80 | 85
Weighted total | 66.5 | 90.5
Five mandatory requirements screened out Concepts 1, 4 and 5; one failure eliminates a concept.
Concept 3 wins on four of five criteria; Concept 2 would need to win every criterion outright to overturn it.

## Slide 14: FINAL CONCEPT: LiSelect·ZW
Input sites, mines, weights
Feasibility gates
Weighted scoring
Cost-optimal selection + allocation
Sensitivity
Report and map
Stack: Next.js + TypeScript on the server, SQLite through Prisma, Leaflet with OpenStreetMap, Recharts.
Pages: Dashboard, Sites, Mines, Criteria and a saved Scenario report.
Principle: gates run first and a score can never compensate for a failed gate.
Traceability: every output number traces to an input, a gate, a weight or a constraint.

## Slide 15: DESIGN CALCULATIONS: CRITERIA, GATES, SCORING
Gate | Pass if
Water supply | ≥ 4 ML/day
Grid reliability | ≥ 0.70
Settlement buffer | ≥ 3 km
Protected land | not on protected land
Plant capacity | ≥ 200,000 t/yr
Land area | ≥ 50 ha
Tailings suitability | ≥ 5 / 10
Feedstock supply | total supply ≥ capacity
15 criteria in 5 groups: Industrial, Logistical, Utility, Land, Environmental; each has a definition, evidence required and source.
Normalise: n = (v − min) / (max − min), clamped 0–1; cost criteria use 1 − n; scaled to 0–100.
Score: S = Σ(w·n) / Σw, so only relative weights matter.
Example: water 8 ML/day on range 0–10 gives n = 80.

## Slide 16: DESIGN CALCULATIONS: OPTIMISATION MODEL
min Σj (Fj + Lj) yj + Σi Σj r · dij · xij
s.t. Σj yj = 1 one facility
Σj xij ≤ Si for all i mine supply
Σi xij = Cj · yj for all j plant capacity
yj = 0 if site j fails a gate feasibility
Variables: yj = 1 if site j is selected; xij = tonnes per year from mine i to site j.
Data: Si mine supply, Cj capacity, dij road km (straight line × 1.3), r haulage rate (USD/t·km), Fj fixed opex, Lj land price × area ÷ 20 years.
Solution: each gate-passing site is solved exactly, cheapest road-km first; the lowest total annual cost wins.

## Slide 17: RESULTS: DEMONSTRATION DATASET
Illustrative Zimbabwe dataset: 5 candidate sites, 5 mines, 1.26 Mt/yr supply, haulage USD 0.25/t·km
Site | Gates | Reason / score
Goromonzi | PASS | Score 67.0 (rank 1)
Kwekwe South | PASS | Score 60.7 (rank 2)
Masvingo East | PASS | Score 56.3 (rank 3)
Insiza (Zulu adjacent) | FAIL | Water 2.8 ML/day; grid reliability 0.55
Mutorashanga Wetland Margin | FAIL | Settlement 1.2 km; protected land; tailings 3.5
Two of five sites are eliminated at the gates, and the failure reasons are recorded for stakeholders.
The three survivors are ranked by weighted score and then priced.

## Slide 18: RESULTS: COST AND ALLOCATION
Chart: Annual cost (USD million)
| Goromonzi | Kwekwe South | Masvingo East
Haulage | 3.22 | 24.07 | 22.1
Fixed opex | 3.2 | 2.9 | 2.6
Land amortisation | 0.09 | 0.05 | 0.05
Mine | t/yr | Road km | Cost
Arcadia | 420,000 | 5 | $0.48M
Bikita | 30,000 | 366 | $2.75M
Total | 450,000 |  | $3.22M
Recommended: Goromonzi at USD 6.52M per year (haulage 3.22M + opex 3.20M + land 0.09M).
Next best: Masvingo East USD 24.75M and Kwekwe South USD 27.02M.
Allocation: nearest mine first, then the rest from the next mine up to its supply limit.
Haulage dominates: Goromonzi sits 5 km from Arcadia, the largest nearby supplier.

## Slide 19: RESULTS: SENSITIVITY
Haulage rate | Annual cost | Change | Optimal site
USD 0.125 (0.5×) | $4.91M | −24.7% | Goromonzi
USD 0.200 (0.8×) | $5.87M | −9.9% | Goromonzi
USD 0.250 (base) | $6.52M | 0% | Goromonzi
USD 0.300 (1.2×) | $7.16M | +9.9% | Goromonzi
USD 0.500 (2×) | $9.74M | +49.5% | Goromonzi
Mine supply −15%: cost +87.4% (USD 12.2M); Goromonzi still optimal.
Mine supply +15%: cost −41.6% (USD 3.8M); Goromonzi still optimal.
Weights ±10%: no criterion changes the top-scoring site.
ROBUST: the recommendation holds under every tested perturbation
A fragile result is flagged FRAGILE with its reasons, so weak evidence is never hidden.

## Slide 20: ECONOMIC ANALYSIS
Cost of a wrong site (demo data): Masvingo East costs USD 18.2M more per year than Goromonzi, about USD 365M over a 20-year plant life (undiscounted).
Where the money goes: at Goromonzi, haulage 49%, fixed opex 49%, land 1.4%; haulage distance is paid on every tonne for the life of the plant.
Land price is not the decider: land amortisation is under USD 0.1M per year at every feasible site.
Cost of the tool: licence cost USD 0; Next.js, SQLite, Prisma, Leaflet and OpenStreetMap are free and run on a single host.
Caveat: costs cover haulage, fixed opex and land only; capital cost and revenue are not modelled.

## Slide 21: RECOMMENDATIONS
Connect real spatial datasets so protected-area and settlement checks come from geometry, not user assertion.
Add a formal AHP module so weights have a documented provenance.
Replace straight-line distances with routed road-network distances.
Extend allocation to several plants for regional planning.
Validate against real candidate sites and compare with practitioner judgement.
Make gate thresholds editable in the interface.

## Slide 22: CONCLUSION
Objective 1: 15 criteria in 5 groups with definitions and required evidence, plus 8 feasibility gates.
Objective 2: a cost-minimising facility selection and allocation model with capacity, supply and gate constraints.
Objective 3: a web system reporting gate outcomes, annual costs, allocation and sensitivity with a robust or fragile verdict.
Result: repeatable, explainable and defensible site recommendations.
THANK YOU